## Slide 1: Heat Pump Quality Assurance

## Slide 2: QA process for HP installations
1. ASHP Guidance/ Spec Document included as part of HP installer procurement
2. Requirement for certain level of training for lead HP installers
4. Installers submit ASHP designs that meet Guidance/ Spec
8. Installer carries out self-audit before leaving site and submits
3. Any deviations from ASHP Guidance Document agreed with PM before install
6. Heat metering monitoringinstalled on some* ASHP installations (aim 25%)
5. Clerk of Works assess HP installation during and after
9. Carry out audits on first installs of all installers and X% after that
10. Homes revisited to check heating set up and customer satisfaction
Pre-Install
Design
Install
Post-Install
7. Installer carries out commissioning as per guidance/ spec
Metric
1
Metric
2,3
Metric
4
Metric
5

## Slide 3: Proposed Metrics and Evidence
Number | Metric | Evidence
1 | Demonstration that lead heat pump installers meet minimum accreditation in guidance document (including Heat Geek Mastery Course or equivalent) | List of installers and certificate of accreditation
2 | 100% of heat pump systems designed for a max 45 Degrees Celsius flow temperature (unless otherwise agreed) | Designs provided in an accessible format
3 | 100% system performance estimates at 350% or above (unless otherwise agreed) | Designs provided in an accessible format
4 | 100% self-audit forms completed by installer | Self-audit forms
5 | 100% homes are revisited (or attempted to revisit) to check heating set up and customer satisfaction (can be done remotely) | CRM log